## Slide 1: Transport Over IP
รศ.ดร. อนันต์ ผลเพม
Asso. Prof. Anan Phonphoem, Ph.D.
anan.p@ku.ac.th http://www.cpe.ku.ac.th/~anan Computer Engineering Department Kasetsart University, Bangkok, Thailand

## Slide 2: Outline
Transport Layer
Transport Layer
User Datagram Protocol (UDP)
Transmission Control Protocol (TCP)
Stream Control Transmission Protocol
(SCTP)
Real-Time Transport Protocol (RTP)

## Slide 3: TCP/IP protocol Suite
Application | 
TCP | UDP
IP | 
Datalink | 
Physical | 

## Slide 4: TCP/IP protocol Suite
Application
Transport
Network
Application
Transport
Network
Network
Data Link Physical
Data
Phy
Data
Phy
Physical
Data Link
Notes: สองด้านซ้ายขวาไม่จำเป็นต้อง Implement network เดียวกัน
Transport วิ่งข้ามตัวกลางเลย แต่ปัจจุบันอาจไม่จริงแล้วก็ได้

## Slide 5: Issues in Network Layer
No/Little error detection
No attempt to correct
  Retransmission
Connectionless
No handshaking
No verification
No flow control

## Slide 6: Transport Protocol
Set of rules
  for exchange control message / data
End-to-End
Application may by-pass Transport Protocol
  build functions on top of IP
  reduce overhead
  application runs on switch/router that has
no Transport Layer

## Slide 7: Transport Protocols
User Datagram Protocol (UDP)
Transmission Control Protocol (TCP)
Stream Control Transmission Protocol (SCTP)
Real-Time Transport Protocol (RTP)

## Slide 8: Ports and Addresses
IP address is the end point of identifier
  source / destination
On same machine (same IP)
  needs identifier for each application
  multiple applications (e.g. 3 Ftp sessions)
“Port”
  16-bit number (65,536 ports) for each IP

## Slide 9: Ports and Addresses
IP address: 158.108.1.2
Unique connection identifier [source IP] + [source port] [dest. IP] + [dest. port]
Web #1 [158.108.1.2:80]
Web #2 [158.108.1.2:8080]
Ftp [158.108.1.2:20]

## Slide 10: Ports and Addresses
Known destination IP
Concern Issues
  destination port ?
  listen port ?
IANA divides ports into three ranges
  well-known ports
  registered ports
  dynamic / private ports

## Slide 11: Well-known ports
 1 – 1023
Used by server applications
Use with restricted privileges (root)
Assigned by IANA

## Slide 12: Well-known ports: Examples
Port Number | Description
80 | WWW
25 | SMTP
23 | Telnet
22 | SSH
21 | ftp-control
20 | ftp-data
161 | SNMP

## Slide 13: Registered Ports
 1024 – 49,151
Used for server applications
  Allow client to make contact
Registered with IANA (for uniqueness)
On most systems, registered ports can be
used by ordinary users
Ex. 8080: HTTP alternate
  commonly used for Web proxy and caching server
  or for running a Web server as a non-root user

## Slide 14: Registered Ports: Examples
Port Number | Description | 
1188 | hp-webadmin | HP Web Admin
1376 | ibm-pps | IBM Person to Person Software
1381 | apple-licman | Apple Network License Manager
1741 | cisco-net-mgmt | Cisco network managment

## Slide 15: Example from
http://www.iana.org/assignments/port-numbers

## Slide 16: Dynamic / Private ports
 49,152 – 65,535
Ephemeral ports (one day, temporary)
  as-needed basis
  freed up when done

## Slide 17: Ephemeral
Nature
  “An ephemeral waterbody is a wetland, spring, stream, river, pond or lake that only exists for a short period following precipitation or snowmelt.”
Bio
  “Many plants are adapted to an ephemeral lifestyle, in which they spend most of the year or longer as seeds before conditions are right for a brief period of growth and reproduction.”
Staircase Falls in Yosemite National Park only flows after heavy rainfall or snowmelt
From http://en.wikipedia.org/wiki/Ephemeral

## Slide 18: Ephemeral
From http://en.wikipedia.org/wiki/Ephemeral
Network
  “In computer networking technology, an ephemeral port is a TCP, UDP or SCTP port which is dynamically assigned to a client application for a short period of time (the duration of time the application is running).”
  “This is in contrast to the "well known" ports which are typically statically assigned to a specific application or service.”

## Slide 19: Dynamic / Private ports
 49,152 – 65,535
Ephemeral ports (one day, temporary)
  as-needed basis
  freed up when done
Assigned by local machine
  Not register with IANA
Never used for destination port at start
  used by initiator as the return add.

## Slide 20: Connection-Oriented Transport
Advantages
  easy to communicate (if receiver is there!)
  verify the real receiver
  agree on some protocols
  error correction
Disadvantages
  heavyweight protocol
  sophisticated implementation (keep state)
  consume high bandwidth for management
TCP

## Slide 21: Connectionless Transport
Datagram approach
Advantages
  rapid data transfer
  no connection setup
  no need for connection maintenances
Disadvantages
  not reliable (or fail)
  out of order packets
  application more complex (takes precautions)
UDP

## Slide 22: Outline

User Datagram Protocol (UDP)
Transport Layer
User Datagram Protocol (UDP)
Transmission Control Protocol (TCP)
Stream Control Transmission Protocol
(SCTP)
Real-Time Transport Protocol (RTP)

## Slide 23: User Datagram Protocol (UDP)
Characteristics
  No error detection/recovery
  No flow control
  No checking for existing of destination
Simple services
Very useful protocol

## Slide 24: UDP Encapsulation

## Slide 25: UDP Basic Functions
provide basic functions above raw IP
  Destination port – to specific application
  Source port – for send back info
  Data integrity verification – checksum
  Data reassembly – segmented packets

## Slide 26: UDP well-known ports

## Slide 27: UDP Message Format
Total length = UDP header+ Payload ≤ 216 bytes

## Slide 28: UDP Message Fragmentation
UDP Header
IP Header
DataData
IP Header
UDP Header
Payload
Data
Transport Layer
IP Layer

## Slide 29: UDP Checksum
Why needed it ?
  Data link already provided CRC
  No corrupted frame accepted
Connectionless !
  loss packets due to route
Sender can choose not to use – set to 0
  Optional
  performance issue
Notes: ทำไมต้องทำ crcอีกอ่ะในเมื่อ datalinkก็ทำแล้วละเอียดด้วย
เพราะบางทีข้อมูลหายได้ connectionless เลยอาจมีการเช็คด้วย หรือถ้าเซ็ต0ก็คือไม่ต้องเช็คเลย

## Slide 30: UDP Checksum
Compare to other checksums
  different – UDP pseudo header
  same – 16-bit one’s complement
At sender
  create pseudo header
  Add zero to checksum field
  calculating checksum of pseudo header + regular header + message
  discard pseudo header when finished
Notes: การทำงาน
สร้าง สูโดมาแล้ว set 0 ก่อน

## Slide 31: UDP Checksum
At receiver
  create pseudo header
  save received checksum
  change checksum to zero
  calculating checksum (pseudeo+regular
header+message)
  compare the calculate and save value

## Slide 32: Why Pseudo Header is needed?
UDP Header
  Only source/destination ports in the header
  No Destination IP Address
    IP Header contains IP add.
Reduce size of UDP Header
Need to check for correct destination
Notes: UDP มีแต่portนะไม่มี IP

## Slide 33: UDP Pseudo Header
Pseudoheader
Source IPv4 Address |  |  | 
Destination IPv4 Address |  |  | 
rsev (0) 8 bits | Protocol Type (UDP = 17) | UDP Length 16 bits | 
Source Port 16 bits |  | Destination Port 16 bits | UDP header
UDP Datagram Length 16 bits |  | UDP checksum 16 bits | 
Data |  |  | 
0
31
Notes: สร้างหัวเทียมขึ้นมาแล้วรวมกับ header แล้วคำนวนใหเสร็จแล้วโยนทิ้งไปแล้วส่งตัวล่างไปทำให้ไม่หนักหัว
ขอกลับก็ทำเช่นกัน ทำให้ไม่ต้องใส่ ip

## Slide 34: UDP Checksum
If error found
  discard packet
  responsibility of application
IPv6
  Pseudo header is v6
  checksum is mandatory
Notes: Error ก็ทิ้งไปดิ

## Slide 35: Protocols that use UDP
TFTP (trivial FTP)
BOOTP (for diskless station)
Network Time Protocol (NTP)
  need basic delivery and checksum
Network File System (NFS)
  need low overhead
Link Management Protocol (LMP)
  original use raw IP (has its own error process)
  move to UDP (preserve scarce IP protocol identifier)
Label Distribution Protocol (LDP)
  need to support multicast and broadcast
  discovery mechanism

## Slide 36: UDP Lite
Ultra-lightweight version
Codecs for voice / video
  good at handle error in data streams
  need UDP not to discard damage packets (RF error message) based on checksum
  remove checksum for better performance
UDP Lite applies checksum to part of packet
  Sensitive part (e.g. address ; not payload)
  whole packet sensitive  regular UDP packet
Notes: เป็นไปได้มั้ยให้มันเบากว่านั้นอีก UDP Lite โคตรๆเบา

## Slide 37: UDP Lite Header
Source Port 16 bits | Destination Port 16 bits
UDP Datagram Length 16 bits | UDP checksum 16 bits
regular UDP header
Checksum Coverage Field
16 bits
UDP checksum
16 bits
UDP Lite header
# of bytes in UDP header that included in the checksum 0 = all bytes not included
UDP datagram Length = same as regular UDP
Source Port 16 bits | Destination Port 16 bits
Checksum Coverage Field 16 bits | UDP Lite checksum 16 bits