## Slide 1: Network Layer & IPv4
(Part II)
รศ.ดร.อนันต์ ผลเพ่ม
Assoc. Prof. Anan Phonphoem, Ph.D.
anan.p@ku.ac.th http://www.cpe.ku.ac.th/~anan Computer Engineering Department Kasetsart University, Bangkok, Thailand
2016

## Slide 2: Outline
Network Layer
IP Fundamental Operation
Internet Protocol
Addressing

## Slide 3: IP Address
32 bits
32 bits

## Slide 4: IP Address
Address space of IPv4 (32 bits)
 232 = 4,294,967,296
Unique and Universal
  Local & Global Sense
Assigned by National Registries
Subset from Internet Corporation for Assigned Names and Number (ICANN)
Does an IP address represent a machine ?

## Slide 5: Internet Address

## Slide 6: Internet Classes
Classfull Addressing

## Slide 7: IP Address Class

## Slide 8: Amount of Networks and Hosts

## Slide 9: IP address in decimal notation
1 1 1 0
x
x
x
x
158.108.2.61
10011110 01101100 00000010 00111101
1 0 0 1
x x x x
27 26 25 24
128 + 16 +
23 22 21 20
8 + 4
+ 2 + = 158

## Slide 10: IP address practice
10011110
00001100
201.125.137.213
01101100 00100000 00010010 158.108#.312.18
00011001 00000001 00010111 12.25.1.#232
11001001 01111101#310001001 11010101

## Slide 11: IP address in decimal notation
10011110
01101100
00000010
00111101
158.108.2.61
www.ku.ac.th
How about iwing.cpe.ku.ac.th ?

## Slide 12: Class Ranges

## Slide 13: IP Address Class
A 50%
B
25%
C 12.5%
D
E

## Slide 14: IP Address Blocks

## Slide 15: Special IP Addresses
This computer Address (all 0; e.g. 0.0.0.0)
Loopback Address
Broadcast Address
Private IP Address
Network Address

## Slide 16: Special IP Address: Loopback Address
โปรเซส A
โปรเซส B
ไอพ
เดทาลงิิ ค ฟิิสคิิ ล
ีี ลปูู แบค็็ อนิิ เทอรเ์์ ฟส
ทซีี พีี /ีี ยดูู พีี ีี 127.0.0.1
แอดเดรสอน่่ืื ๆ
แพก็็ เกต็็ ผา่่ น
ลปูู แบค็็ อนิิ เทอรเ์์ ฟส เขา้้ สอูู่่ กีี โปรเซสหน่่ึึง
์์ แพก็็ เกต็็ ถกูู ส่่งเขา
ลปูู แบค็็ อนิิ เทอรเ์์ ฟส
127.0.0.0/8  127.0.0.1

## Slide 17: Special IP Address: Broadcast Address
Ending with 255
Use for sending to all nodes in class range
Directed Broadcast Address
  all hosts = 1
  Class A broadcast: 10.255.255.255
 Class B broadcast: 158.108.255.255
  Class C broadcast: 202.100.15.255
Limited Broadcast Address
 all 1; e.g. 255.255.255.255

## Slide 18: Special IP Address: Private IP Address
Class A (1 group)
 10.0.0.0 – 10.255.255.255
Class B (16 groups)
 172.16.0.0 – 172.31.255.255
Class C (256 groups)
 192.168.0.0 – 192.168.255.255

## Slide 19: Special IP Address: Network Address

## Slide 20: Sample internet
Network and Host addresses

## Slide 21
A Network with
Two Levels of Hierarchy

## Slide 22
A Network with
Three Levels of Hierarchy

## Slide 23
Addresses
with and without Subnetting

## Slide 24: Finding a Network Address

## Slide 25: Network Address

## Slide 26: Masking (without subnet)
IP Address: Binary IP Address:
141 . 14 . 2 . 21
1000 1101 . 0000 1110 . 0000 0010 . 0001 0101
Mask: Binary Mask:
255 . 255
1111 1111 . 1111 1111
. 0 . 0
. 0000 0000 . 0000 0000
Network Address: Binary IP Address:
141 . 14 . 0 . 0
1000 1101 . 0000 1110 . 0000 0000 . 0000 0000
&

## Slide 27: Masking (with subnet)
IP Address: Binary IP Address:
141 . 14 . 2 . 21
1000 1101 . 0000 1110 . 0000 0010 . 0001 0101
. 255
. 0
Mask:
Binary Mask:
255 . 255
1111 1111 . 1111 1111
. 1111 1111 . 0000 0000
141 . 14 .
2
. 0
Network Address: Binary IP Address:
1000 1101 . 0000 1110 . 0000 0010 . 0000 0000
&

## Slide 28
 |  | Default Mask |  |  | 
 | Class |  | In Binary | In Dotted- Decimal | Using Slash
 | A |  | 11111111 00000000 00000000 00000000 | 255.0.0.0 | /8
 | B |  | 11111111 11111111 00000000 00000000 | 255.255.0.0 | /16
 | C |  | 11111111 111111111 11111111 00000000 | 255.255.255.0 | /24

## Slide 29: Example
A router receives a packet with the destination address 201.24.67.32. Show how the router finds the network address of the packet.
Solution
Class C  default mask = 255.255.255.0
67

## Slide 30: Subnet Design
Given a network 194.30.12.0 with 16 hosts in each subnetwork
Find the following:
  The number of subnetworks
  Sub-network ID / Broadcast Address
  Sub-netmask
  First/Last address that can be used for each subnet

## Slide 31: Subnet Design
192.30.12.0
Class C IP address
Last Byte(Host ID)
16 Hosts  24 =16 is not enough (subnetID and broadcast)
 25 = 32  total of 30 hosts
 5 bits for Host and 3 bits for subnet
Subnet |  |  | Host |  |  |  | 

## Slide 32: Subnet Design
.1 1 1 0 0 0 0 0
Subnet Mask
Subnet
Host
255 .
255 .
.
.
.
224
Subnet ID
.
. 00000000 = 0
.
.
. 00100000 = 32
. 01000000 = 64
255
255
30
30
30
30
30
255
255
12
12
12
12
12
194 .
194 .
194 .
194 .
194 .
.
.
. 01100000 = 96
. 10000000 = 128
194 . 30 | . 12 | . 10100000 = 160
194 . 30 | . 12 | . 11000000 = 192
194 . 30 | . 12 | . 11100000 = 224

## Slide 33
 |  | Subnet Design |  |  |  | 
Subnet |  |  | Subnet ID | 1st Add | Last Add | Broadcast
0 |  |  | 192.30.12.0 | 192.30.12.1 | 192.30.12.30 | 192.30.12.31
1 |  |  | 192.30.12.32 | 192.30.12.33 | 192.30.12.62 | 192.30.12.63
2 |  |  | 192.30.12.64 | 192.30.12.65 | 192.30.12.94 | 192.30.12.95
3 |  |  | 192.30.12.96 | 192.30.12.97 | 192.30.12.126 | 192.30.12.127
4 |  |  | 192.30.12.128 | 192.30.12.129 | 192.30.12.158 | 192.30.12.159
5 |  |  | 192.30.12.160 | 192.30.12.161 | 192.30.12.190 | 192.30.12.191
6 |  |  | 192.30.12.192 | 192.30.12.193 | 192.30.12.222 | 192.30.12.223
7 |  |  | 192.30.12.224 | 192.30.12.225 | 192.30.12.254 | 192.30.12.255