## Slide 1: CIDR – VLSM – AS
รศ.ดร. อนันต์ ผลเพม
Asso. Prof. Anan Phonphoem, Ph.D.
anan.p@ku.ac.th http://www.cpe.ku.ac.th/~anan Computer Engineering Department Kasetsart University, Bangkok, Thailand

## Slide 2: Outline
Classless Interdomain Routing (CIDR)
Variable Length Subnet Mask (VLSM)
Autonomous System (AS)

## Slide 3: IP Addresses Revisited
Potential exhaustion of IPv4 address space
(due to inefficiency)
  Class B is too big
  Class C is too small (many are available)
Growth of back bone routing tables
  Lots of small networks causes large routing tables
  Route calculation and management requires high computational overhead
Notes: ปัญหา ip ใหญ่เกินไปหรือเล็กเกินไป และปัญหาของการหาเส้นทาง(Routing table)

## Slide 4: Classless InterDomain Routing (CIDR)
Try to balance two competing effects
  Address utilization
  Router complexity
CIDR allows routers to break the rigid interpretation of IP address structures
Also called “Supernet”
  Opposite of “Subnet”
Notes: พยายามให้ใช้มากสุดคือ ทำไงให้ router และการจัดการ addressให้ดีที่สุด CIDR ยอมให้ Router break RIGID ทิ้งไปเลย เรียก SUPERNET

## Slide 5: Classful & Classless addressing
5
16K networks x 64K hosts
128 networks x 16M hosts
A
B
2M networks x 256 hosts
C
Obsolete
inefficient
depletion of B space
too many routes from C space
Classful
Classless
Best Current
Practice
Classful
1 C
...
16 C
32 C
64 C
128 C
1 B
...
Hosts
2
4
8
16
32
64
128
256
... 4096
8192
16384
32768
65536
...
Prefix
/31
/30
/29
/28
/27
/26
/25
/24
...
/20
/19
/18
/17
/16
...
Notes: เปลี่ยนไปใช้เป็น Classless เวลาเขียนก็จะเขียนด้วย slaash

## Slide 6: Prefix Length

## Slide 7: CIDR Example
Address in binary:
10100111 11000111 10101010 01010010
Keep the left 27 bits: 10100111 11000111 10101010 01000000
What is the first address in the block if one of the addresses is 167.199.170.82/27?
Solution
Result in CIDR notation: 167.199.170.64/27
Notes: โจทย์ อะไรคือ ADDRESS แรก ก็คือ .65

## Slide 8: Supernetting: CIDR
Enable network number to be any length (No Class)
Collapse multiple addresses assigned to a single AS to
one address
All routers must understand CIDR addressing
  Need both Address and Mask (prefix and suffix)
 Slash notation (123.10.16.0 /20)
Some prefixes are reserved for private add.
 10/8, 172.16/12, 192.168/16, 169.254/16
  These are not routable in the Internet
Notes: ความยาวเท่าไหร่ก็ได้ ทำการAddress หลายๆอันมารวมเป็น 1 Address และ router ทุกตัวต้องรองรับ CIDR ใช้ SLASH Notation

## Slide 9: Example of CIDR
ISP
Company C
Company B
Consider an ISP providing IP connection to a number of private companies
If IP addresses for companies are carefully selected
  a border router needs only advertise one
“aggregated” route for all companies
Company A
Advertise Route
Notes: ตัวอย่าง Company A,B,C อยู่ภายใต้ ISP เดียวกันถ้าAddressแต่ละอันถ้าให้ IP ดีพอจะ Manage Grouping ได้ ถ้าISP ต่อกับGateway ประเทศ จะส่งสามบริษัทหรือส่งชื่อเดียว

## Slide 10: Example of CIDR (Supernetting)
If ISP needs 16 class C addresses
  make them contiguous
 Eg. 199.23.16.0 to 199.23.31.0
  enables a 20-bit network number
199.23.0001
199.23.0001
199.23.0001
199.23.0001
… 199.23.0001
0000.0  199.23.16.0
0001.0  199.23.17.0
0010.0  199.23.18.0
0011.0  199.23.19.0
1111.0  199.23.31.0
Notes: ทำให้Contiguous เรียงกัน ถ้าประกาศชื่อต้องการประกาศเบอร์เดียวมั้ย ถ้าประกาศrouteตรงไปตรงมา 16วงจะมา AND ทีละตัว แล้วเทียบตาราง แล้วโยนออก ได้มา16 link
แต่ถ้าเรียนมา มัน contiguous เป็นไปได้มั้ยจะเอาเบอร์เดียว คือประกาษเป็น 20 enable ควรประกาษเป็น199.23.16.0 แล้วพอ route ไปแล้วก็จบรู้เบอร์เดียวก็พอ จากตอนแรก/24 ไปเป็น/20

## Slide 11: Example of CIDR
199.23.16.0
199.23.17.0
…
199.23.31.0
11
Without CIDR
199.23.16.0
199.23.17.0
…
199.23.31.0
Boarder Gateway
With CIDR
199.23.16.0/20
Notes: ถ้าจะไปวงนี้ให้โยนมี BoarderGateWay เยอะentry
แต่ถ้าทำ CIDR คือสามารถโยนไป1entry เท่านั้นเพื่อให้ routeจัดการ

## Slide 12: Aggregation
Some pairs of consecutive prefixes
Example: routes within the same AS:
AS has 2 address blocks:
1.2.2.0/24 =
1.2.3.0/24 =
0000001.00000010.0000001
0000001.00000010.0000001
0.00000000/24
1.00000000/24
Can announce 1.2.2.0/23
12
Notes: เลื่อนขึ้นมา1อันก็ได้ จะทำให้สามารไปดั้ง 2 route ได้ เป็นการทำ route Aggregation
แต่ถ้าประกาศผิด คือการรวม routeคนอื่นมาด้วย ทำให้ network traffic หายเรียบ แล้วก็โดนแบน เพราะnetwork ที่ส่งมาหาย แล้วคนที่จะรับจริงๆก็ไม่ได้รับ network ใดๆเลย
ในข้อสอบห้ามเลื่อน Bit ผิด

## Slide 13: CIDR: Longest prefix match
124.39.0.0/16
124.39.11.0/24
124.39.11.0/24
124.39.0.0/16
124.39.11.32
124.39.22.45
13
Because prefixes of arbitrary length allowed, overlapping prefixes can exist.
Example:
router hears 124.39.0.0/16
from one neighbor
and 124.39.11.0/24 from another neighbor
Router forwards packet according to most specific forwarding information, called longest prefix match
  Packet with destination 124.39.11.32 will be forwarded using /24 entry.
  Packet with destination 124.39.22.45 will be forwarded using /16 entry
Notes: อาจเกิด Overlapping ได้เพราะประกาศกว้างกว่า
ก็เช็คว่าอันไหนตรงก็ส่งไป

## Slide 14: CIDR: Longest prefix match
14
Implicit ordering in the routing table
  longer prefixes higher up the table
  So, the first match is the right one
Explicit route to directly attached host
  a netmask of 0.0.0.0

## Slide 15: VLSM

## Slide 16: VLSM
Variable-length subnet mask
Classful allows only one subnet in a network
  > one subnet in an autonomous system
Maximizing the use of address (Subnet Zero)
“Subnetting a Subnet”
Routing Protocol that supports VLSM
  OSPF, Integrated IS-IS, EIGRP, RIPv2, and static
routing

## Slide 17: Subnet with VLSM
192.168.10.0/24

## Slide 18: Regular Subnet
7 subnets; The largest subnet needs 60+1 hosts
If 3 bits for subnet (8 subnets)  5 bits for host (32 hosts)
If 6 bits for host (64 hosts)  2 bits for subnet (4 subnets)
192.168.10.0/24

## Slide 19: Subnet with VLSM
Perth
KL
Select the biggest first
 192.168.10.0/24
 192.168.10.0/26

192.168.10.64/26
 192.168.10.128/26
 192.168.10.192/26
192.168.10.64/26
 192.168.10.64/27
 192.168.10.96/27

## Slide 20: Subnet with VLSM
 192.168.10.96/27
 192.168.10.96/28
 192.168.10.112/28
 192.168.10.128/26
 192.168.10.128/30
 192.168.10.132/30
 192.168.10.136/30
 192.168.10.140/30
 ...
Sydney
Singapore
Perth – KL Sydney – KL Singapore – KL

## Slide 21: Final: Subnet with VLSM

## Slide 22: Example II
CPE
IE
EE
165.23.208.0/20
700 Stations
500 Stations
100 Stations
250 Stations
165.23. 1101 0000 . 0000 0000

## Slide 23: Solution
•165.23.208.0/20
•165.23.208.0/22
•165.23.212.0/22
•165.23.216.0/22
•165.23.220.0/22
•165.23.212.0/22
•165.23.214.0/24
•165.23.215.0/24
•165.23.215.0/24
•165.23.215.128/25
•165.23.215.128/25
•165.23.215.128/30
•165.23.215.132/30
•165.23.215.136/30
•…
1022 Hosts
•165.23.212.0/23 510 Hosts
•165.23.214.0/23
•165.23.214.0/23
254 Hosts
•165.23.215.0/25 126 Hosts
2 Hosts
The largest subnet needs 701 hosts
10 bits for host (1024 hosts)
CPE
IE
EE
700 Stations
500 Stations 100 Stations
250 Stations

## Slide 24: Final Solution
CPE
IE
EE
165.23.208.0/20
700 Stations
500 Stations
100 Stations
165.23.208.0/22
165.23.214.0/24
250 Stations
165.23.215.128/30
165.23.215.132/30
165.23.212.0/23
165.23.215.0/25

## Slide 25: Quiz
100 hosts
80 hosts
550 hosts
100 hosts
100 hosts
30 hosts
15 hosts
A
ZZ
B
C
D
113.12.128.0/17

## Slide 26: Notes for CIDR
CIDR was actually intended as a quick fix
  Solve addressing crisis until IPv6 was deployed
Unfortunately, CIDR has been widely
adopted
  IPv6 deployment has proven to be very, very
slow
CIDR is currently deployed
  However, IPv6 is not compatible with IPv4
  Generates a big migration problem

## Slide 27: Growth in Routing Table Size
Pre-CIDR (1988-1994): Steep Growth Rate
“Jennifer Rexford”, Internet Routing (COS 598A)

## Slide 28: Growth in Routing Table Size
CIDR Deployment (1994-1996): Much Flatter
“Jennifer Rexford”, Internet Routing (COS 598A)

## Slide 29: Autonomous System (AS)
A single network domain
Grouping of computers/routers
Operate in isolation from other groups
A single network administrative entity

## Slide 30: Autonomous System (AS)
Need protocols for distribute routing information in the AS
  Interior Gateway Protocols (IGPs)
  Intradomain routing algorithms
Between AS
  Need interdomain routing algorithms
  Exterior Gateway Protocols (EGPs)
  More complex task

## Slide 31: Autonomous System (AS)
AS 1
AS 20
AS 5
AS 7
Autonomous System
Boarder router (ASBR)
Exterior Gateway Protocol (EGP Link)
Interior Gateway Protocol (IGP Link)
This is the Internet !

## Slide 32: Types of AS
Stub AS
  Only has a single connection to one other AS
  only carries local traffic
Multihomed AS
  Connect to more than one other AS
  But will not carry transit traffic
Transit AS
  Connect to more than one other AS
  Can carry both local and transit traffic

## Slide 33: Transit vs. Nontransit AS
Transit traffic = traffic whose source and destination are outside the AS
AS1
ISP1
ISP2
r1
r2
r2
r3
r2
r1
r3
Nontransit AS: does not carry transit traffic
Advertise own routes only
Do not propagate routes learned from other AS’s
AS1
ISP1
ISP2
r1
r2,r3
r2,r1
r3
r2
r1
r3
Transit AS: does carry transit traffic
Advertises its own routes PLUS routes learned from other AS’s