## Slide 1: Routing III
รศ.ดร. อนันต์ ผลเพ่ม
Asso. Prof. Anan Phonphoem, Ph.D.
anan.p@ku.ac.th http://www.cpe.ku.ac.th/~anan Computer Engineering Department Kasetsart University, Bangkok, Thailand

## Slide 2: Outline
Intermediate-System to Intermediate- System (IS-IS)
Border Gateway Protocol (BGP)
IPv6 Routing

## Slide 3: Routing Protocol
IGP (Interior Gateway Protocol)
  Exchange routing info. within an AS
  RIP, IGRP, EIGRP, OSPF
EGP (Exterior Gateway Protocol)
  Exchange routing info. between AS
  BGP
Autonomous System (AS) [RFC 1771]
  “A set of routers under the single technical administration, using an IGP and common metrics to route packets within the AS, and using an EGP to route packets to other AS’s.”
Notes: Igp แตกเป็น LINK กับ RIP
EGP แตกเป็นpath

## Slide 4: Internet - Early Age
EGP Restriction:
•Tree only
•One Backbone
EGP
EGP
EGP
EGP
EGP
IGP
AS 2
EGP
EGP
IGP
AS 1
EGP
EGP
Internet Backbone

## Slide 5: Internet – Current State
BGP-4
ISP1
IGP
BGP-4
BGP-4
BGP-4
BGP-4
BGP-4
BGP-4
BGP-4
BGP-4
BGP-4
IGP
IGP
ISP2
ISP3
ISP Connection
•Tree -> Graph
Notes: แต่ละหน่วยงานจะคุยกันต่างๆ กัน แต่แตละ จะคุยด้วยBGP เป็นตัวแทนของexterior

## Slide 6: Autonomous System (AS)
AS 1
AS 20
AS 5
AS 7
Autonomous System
Boarder router (ASBR)
Exterior Gateway Protocol (EGP Link)
Interior Gateway Protocol
(IGP Link)
This is the Internet !

## Slide 7: Border Gateway Protocol
BGP
BGP-4
Concentrate on Loop-Free > lowest cost
Based on policy
  e.g. lowest # of AS
  Need to go through AS 12
Advanced distance vector routing protocol
  Path Vector routing protocol
Notes: อยู๋ที่ขอบเป็นตัวที่link ระหว่าง AS เน้นLoop free
แล้วbased on policy
มี Path vector routing

## Slide 8: Path Vector Routing
Limitation of Distance vector / Link state
  Interior routing protocol (Intra-Domain/AS)
Exterior routing protocol (Inter-Domain/AS)
Router holds
  a list of networks that can be reached with the path (ASs to pass)
  x.x.x.x can be reached through AS y
 RFC 1772
Notes: ไม่สามารถสเกลได้
จะเป็นList ของเครือข่ายต่างๆที่สามารถไปถึงได้

## Slide 9: Path Vector Routing Analogy
9
National map (Distance Vector)
road, city, distance
International Map (Path Vector) existing of cities in each country should be passed to reach destination

## Slide 10: Path Vector Routing Example
Notes: ข้างในคุย OSPF ข้างนอกคุย BGP

## Slide 11: Path Vector Routing Example
Notes: Path vector routing คือ จากไทยไปจีน หรือ ก็คือ จากนอกๆ เช่นจะไป 18 ก็ไป As1, AS2, AS3 ตามลำดับไรงี้
แล้วมันจะรวบอะไรที่เหมือนกันให้เป็นแบบล่าง เพื่อความสั้นลโดยเปลี่ยน / เอา

## Slide 12: Border Gateway Protocol (BGP)
Creating a BGP “peering” relationship involves an interesting combination of trust and mistrust
“Your ISP will show little patience with you if you make mistakes in your BGP configuration”

## Slide 13: BGP Route Selection
N4 AS 4
N5 AS 5
N6 AS 6
N7 AS 7
N2 AS 2
N3 AS 3
N1 AS 1
4.0.0.0
14.0.0.0
5.0.0.0
6.0.0.0
7.0.0.0
17.0.0.0
N2 ประกาศเสน้้ ทาง
(<4.0.0.0, 14.0.0.0, 5.0.0.0>,
<AS 2>) ให้้ N1
N1 ประกาศเสน้้ ทาง
(<4.0.0.0, 14.0.0.0, 5.0.0.0>,
<AS1, AS 2>) ให้้ N3

## Slide 14: Route Announcement: no CIDR
internet
202.0.1.0/242, 02.0.32.0/24,
202.0.2.0/242, 02.0.33.0/24,
202.0.3.0/24
202.0.0.0 - 202.0.255.0
ISP 3
IISSPP 11
202.0.32.0 - 202.0.47.0
202.0.0.0 - 202.0.15.0
202.0.2.0
202.0.3.0
202.0.32.0
202.0.33.0
202.0.1.0/24,
202.0.2.0/24,
202.0.3.0/24
202.0.32.0/24,
202.0.33.0/24
ISP 2
202.0.1.0
Notes: ทำการ Aggregate ให้ดีๆ

## Slide 15: Route Announcement: with CIDR
202.0.1.0
อนิิิ เทอรเ์์ น็็็ต
202.0.0.0//1166
202.0.0.0/16
ISP 3
ISP 1
202.0.32.0/20
202.0.0.0/20
202.0.2.0
202.0.3.0
202.0.32.0
202.0.33.0
202.0.0.0/20
202.0.32..00///222000
ISP 2

## Slide 16: BGP Hazards -- Scenario
Suppose, that through some misconfiguration you advertise 207.46.0.0/16 to your ISP.
Your ISP does not filter out and advertise to the
Internet.
This CIDR block belongs to Microsoft, and you have just claimed to have a route to that destination.
Many decide that the best path to Microsoft is through
your domain.
Flood of unwanted packets (black-holed traffic that
should have gone to Microsoft)
They will be neither amused nor understanding.
By Rick Graziani
Notes: เกิดจากการ Configure ผิด
Configure ว่าไปmicrosoftได้ทุกคนก็ไปทางนี้ซึ่งจริงๆไปไม่ได้ สุดท้ายก็พังกันหมด

## Slide 17: BGP Basics
BGP uses a list of AS numbers through which
a packet must pass to reach a destination.
The function of BGP is to:
  Exchange routing information between AS
  Guarantee the selection of a loop free path.
Notes: การอัปเดต BGP จะ Carry บน TCP คือ Reliable มาก และต้องไม่เป็น loop

## Slide 18: BGP Basics
BGP4
  first version of BGP that supports CIDR and route aggregation.
Common IGPs such as RIP, OSPF, and EIGRP
use technical metrics.
  BGP does not use technical metrics.
Routing decisions based on
  network policies, or rules
BGP does not show the details of topologies within each AS.
BGP sees only a tree of AS
18
Notes: BGP4 support Fiber
Base on policies ต้องผ่านเมืองนี้ๆ เท่านั้น และไม่show detail ของแต่ละ asรู้แค่จากกรุงเทพต้องลงปักกิ่ง

## Slide 19: BGP Basics
BGP updates are carried using TCP on port 179.
  In contrast, RIP updates use UDP port 520
  OSPF, IGRP, EIGRP does not use a Layer 4 protocol
Because BGP requires TCP, IP connectivity must
exist between BGP peers.
TCP connections must also be negotiated between them before updates can be exchanged.
Therefore, BGP inherits those reliable, connection-oriented properties from TCP.
Notes: BGP ต้องใช้ TCP

## Slide 20: Loop free Path
AS Path: 10,20,30,40
AS 10
AS 20
AS 30
AS 40
AS Path: 10
AS Path: 10,20
AS Path: 10,20,30
AS Path: 10,20,30,40
BGP views the whole internetwork as a graph, or tree, of AS
Notes: 20 ซ้ำก็โยนทิ้งไปไม่ยอมให้เกิดลูป

## Slide 21: BGP Operation
21
When two routers establish a TCP- enabled BGP connection between each other, they are called neighbors or peers.
Each router running BGP is called a BGP speaker.
Notes: มันจะสร้าง neighbor section เข้าหากันหรือการทำpeer เรียก BGP Speaker

## Slide 22: Exchange and Update
Exchange Incremental updates
Withdraw route
Peers exchange keepalive messages (e.g. 60 sec for Cisco)
to ensure the connection is maintained.
Notes: หลังจากทำ TCP เรียบร้อย Reliable นะก็จะเริ่ม Exchange กันแบบ Incremental update withdraw ก็เช่นกัน

## Slide 23: BGP Message
There are four BGP message types:
  Type 1: OPEN (After the TCP establishment, both neighbors send Open messages)
  Type 2: KEEPALIVE
  Type 3: UPDATE
  Type 4: NOTIFICATION
All BGP messages are Unicast to the one
neighbor over the TCP connection.

## Slide 24: IPv6 Routing
24

## Slide 25: IPv6 routing
2001:3c8:1303:2222::/64
2001:3c8:1303:3333::/64
2001:3c8:1303:AAAA::/64
2001:3c8:1303:BBBB::/64
2001:3c8:1303:CCCC::/64
2001:3c8:1303:1111::/64
.2
.1
.1
.2
.1
.2
.1
.2
.1
.2
.1
.2
BKK
KPG
SRI

## Slide 26
KPG#show ipv6 route
IPv6 Routing Table - 10 entries
Codes: C - Connected, L - Local, S - Static, R - RIP, B - BGP U - Per-user Static route, M - MIPv6
I1 - ISIS L1, I2 - ISIS L2, IA - ISIS interarea, IS - ISIS summary
O - OSPF intra, OI - OSPF inter, OE1 - OSPF ext 1, OE2 - OSPF ext 2 ON1 - OSPF NSSA ext 1, ON2 - OSPF NSSA ext 2
D - EIGRP, EX - EIGRP external
R 2001:3C8:1303:1111::/64 [120/2]
via FE80::1, Serial0/0/0
C 2001:3C8:1303:2222::/64 [0/0]
via ::, FastEthernet0/0
L 2001:3C8:1303:2222::1/128 [0/0]
via ::, FastEthernet0/0
R 2001:3C8:1303:3333::/64 [120/2]
via FE80::3, Serial0/0/1
2001:3c8:1303:2222::/64
2001:3c8:1303:3333::/64
2001:3c8:1303:AAAA::/64
2001:3c8:1303:BBBB::/64
2001:3c8:1303:CCCC::/64
.1
2001:3c8:1303:1111::/64
.2
.1
.2
.1
.2
.2 .1
.1
.2
.1
.2
C 2001:3C8:1303:AAAA::/64 [0/0]
via ::, Serial0/0/0
L 2001:3C8:1303:AAAA::1/128 [0/0]
via ::, Serial0/0/0
R 2001:3C8:1303:BBBB::/64 [120/2]
via FE80::1, Serial0/0/0 via FE80::3, Serial0/0/1
C 2001:3C8:1303:CCCC::/64 [0/0]
via ::, Serial0/0/1
L 2001:3C8:1303:CCCC::2/128 [0/0]
via ::, Serial0/0/1 L FF00::/8 [0/0]
via ::, Null0
BKK
KPG
SRI

## Slide 27: L – Local ?
Was made to create a corresponding CEF (Cisco Express Forwarding) entry (L3 IP Switching Technology)
Then, the packets destined to this IP address assigned to the router interface can be processed by the router itself
These routes came with the introduction of the IOS feature, Multi Topology Routing (MTR)
Local routes serve a significant function with MTR
27
http://www.ascoltablog.com/what-is-the-l-designation-in-a-cisco-routing-table/

## Slide 28: L – Local ?
interface Ethernet0/0
ip address 10.1.1.1 255.255.255.252
The IP address assigned to Ethernet0/0 is 10.1.1.1/30. This assignment itself is not a host route, but with the proper version of IOS, a Local host route will be installed in the routing table.
R1#show ip route
Codes: L – local, C – connected, S – static, R – RIP, M – mobile, B – BGP
Gateway of last resort is not set
C | 10.0.0.0/8 is 10.1.1.0/30 | variably subnetted, 7 subnets, 2 masks is directly connected, Ethernet0/0
L | 10.1.1.1/32 | is directly connected, Ethernet0/0
 |  | 28
Notes: L คือ Local connect อยู่เพื่อเพิ่มค่าการรันของ CEF

## Slide 29
2001:3c8:1303:2222::/64
via FE80::3, Serial0/0/1
via ::, Null0
2001:3c8:1303:3333::/64
2001:3c8:1303:AAAA::/64
2001:3c8:1303:BBBB::/64
2001:3c8:1303:CCCC::/64
.1
2001:3c8:1303:1111::/64
.2
.1
.2
.1
.2
.2 .1
.1
.2
.1
.2
BKK
KPG
SRI
BKK#show ipv6 route
IPv6 Routing Table - 10 entries
Codes: C - Connected, L - Local, S - Static, R - RIP, B - BGP U - Per-user Static route, M - MIPv6
I1 - ISIS L1, I2 - ISIS L2, IA - ISIS interarea, IS - ISIS summary
O - OSPF intra, OI - OSPF inter, OE1 - OSPF ext 1, OE2 - OSPF ext 2 ON1 - OSPF NSSA ext 1, ON2 - OSPF NSSA ext 2
D - EIGRP, EX - EIGRP external
C 2001:3C8:1303:AAAA::/64 [0/0]
via ::, Serial0/0/0
L 2001:3C8:1303:AAAA::2/128 [0/0]
via ::, Serial0/0/0
 |  | C | 2001:3C8:1303:BBBB::/64 [0/0]
C | 2001:3C8:1303:1111::/64 [0/0] |  | via ::, Serial0/0/1
 | via ::, FastEthernet0/0 | L | 2001:3C8:1303:BBBB::1/128 [0/0]
L | 2001:3C8:1303:1111::1/128 [0/0] |  | via ::, Serial0/0/1
 | via ::, FastEthernet0/0 | R | 2001:3C8:1303:CCCC::/64 [120/2]
R | 2001:3C8:1303:2222::/64 [120/2] |  | via FE80::2, Serial0/0/0
 | via FE80::2, Serial0/0/0 |  | via FE80::3, Serial0/0/1
R | 2001:3C8:1303:3333::/64 [120/2] | L | FF00::/8 [0/0]
Notes: มีC เท่าไหร่มี L เท่านั้น

## Slide 30
2001:3c8:1303:2222::/64
via ::, FastEthernet0/0
via ::, Null0
2001:3c8:1303:3333::/64
2001:3c8:1303:AAAA::/64
2001:3c8:1303:BBBB::/64
2001:3c8:1303:CCCC::/64
.1
2001:3c8:1303:1111::/64
.2
.1
.2
.1
.2
.2 .1
.1
.2
.1
.2
BKK
KPG
SRI
SRI#show ipv6 route
IPv6 Routing Table - 10 entries
Codes: C - Connected, L - Local, S - Static, R - RIP, B - BGP U - Per-user Static route, M - MIPv6
I1 - ISIS L1, I2 - ISIS L2, IA - ISIS interarea, IS - ISIS summary
O - OSPF intra, OI - OSPF inter, OE1 - OSPF ext 1, OE2 - OSPF ext 2 ON1 - OSPF NSSA ext 1, ON2 - OSPF NSSA ext 2
D - EIGRP, EX - EIGRP external
R 2001:3C8:1303:AAAA::/64 [120/2]
via FE80::1, Serial0/0/0 via FE80::2, Serial0/0/1
C 2001:3C8:1303:BBBB::/64 [0/0]
via ::, Serial0/0/0
R | 2001:3C8:1303:1111::/64 [120/2] | L | 2001:3C8:1303:BBBB::2/128 [0/0]
 | via FE80::1, Serial0/0/0 |  | via ::, Serial0/0/0
R | 2001:3C8:1303:2222::/64 [120/2] | C | 2001:3C8:1303:CCCC::/64 [0/0]
 | via FE80::2, Serial0/0/1 |  | via ::, Serial0/0/1
C | 2001:3C8:1303:3333::/64 [0/0] | L | 2001:3C8:1303:CCCC::1/128 [0/0]
 | via ::, FastEthernet0/0 |  | via ::, Serial0/0/1
L | 2001:3C8:1303:3333::1/128 [0/0] | L | FF00::/8 [0/0]

## Slide 31: RIPng
http://computernetworkingnotes.com/ipv6-features-concepts-and-configurations/routing-with-ipv6.html
Routing Information Protocol next generation
Similar to RIP for IPv4
  Based on RIPv2
  Distance vector protocol
  hop-count limit is 15
  Split horizon and poison reverse are used to prevent routing loops

## Slide 32: RIPng
http://computernetworkingnotes.com/ipv6-features-concepts-and-configurations/routing-with-ipv6.html
Routing Information Protocol next generation
Enhancements
  An IPv6 packet is used to transport the routing
update
  ALL-RIP routers multicast address (FF02::9) is used as the destination address in routing advertisements (UDP port 521)
  Routing updates contain the IPv6 prefix of
the router and the next-hop IPv6 address
Enabling RIPng
  Router(config)# ipv6 router rip tag
Notes: ตอนนี้ V6 มีprefixแบบนี้ต้องทำไงๆๆ

## Slide 33: OSPFv3
http://computernetworkingnotes.com/ipv6-features-concepts-and-configurations/routing-with-ipv6.html
Link-state routing protocol
Adjacencies and next-hop attributes now use link-local addresses
Still uses multicast traffic to send its
updates and acknowledgments
  FF02::5 for OSPF routers
  FF02::6 for OSPF-designated routers
  These new addresses are the replacements for
224.0.0.5 and 224.0.0.6, respectively

## Slide 34
KU and
Thailand Interconnection Network

## Slide 35: Internet
Thaisarn
Uninet
OCS
LIB
ENG
50Year
KPS
SRI
CSC
RAT
NOP
SATIT
OCS
1G
1G
1G
34M
2M
100M
2M
6M
24 April 2005
2M
Area 1
Area 2
Area 3
SCI
Area 5
Area 4
Area 10
Firewall & Shaper & Cache
Area 11
34M
Area 12
Area 13
SPN
Area 0
1GKU Gateway
512K
Notes: เกษตรออกไปได้สองทางไทยสาน ยูนิเน็ต รูปถัดไป

## Slide 36
36

## Slide 37
37

## Slide 40
40

## Slide 41: National – Feb 2010

## Slide 42: International - Feb 2010

## Slide 43: References
CCNP slide by Rick Graziani, Cabrillo College, Feb. 2004
Internet Information Research Center
(IIRC)
  http://iir.ngi.nectec.or.th