## Slide 1: Multiprotocol Label Switching
1
(MPLS)
รศ.ดร. อนันต์ ผลเพ่ม
Asso. Prof. Anan Phonphoem, Ph.D.
anan.p@ku.ac.th http://www.cpe.ku.ac.th/~anan Computer Engineering Department Kasetsart University, Bangkok, Thailand

## Slide 2: Outline
1
Motivation
MPLS Basics
Operation
Protocol Stack Architecture
Advantages and Disadvantages

## Slide 3: Motivation
1
IP
ATM
MPLS positioning

## Slide 4: Internet Protocol (IP)
1
IP is here and everywhere
De facto protocol for global Internet
Disadvantages
  connectionless (e.g. no QoS)
  independent forwarding decisions based on IP
  large IP header (at least 20 bytes)
  routing in Network Layer (Slower than Switching)
  Usually shortest path (not concern other metrics)

## Slide 5
Asynchronous Transfer Mode
(ATM)
5

## Slide 6: Packet Sizes in the Network
traffic unpredictable
Slow and expensive
Delay variation
5

## Slide 7: Voice Transmission
5
If introduce large packet size for voice
  Cannot tolerate long delay, large jitter
  Echo problem
    echo cancellation does not work (long delay)
To support voice
  Small packet
  fixed-size packet
  Called “Cell”  ATM cell

## Slide 8: Multiplexing using cells
Advantages of cells
Fair delay
high speed and cheap (switching and multiplexing -> HW)
5

## Slide 9: An ATM cell
VPI: Virtual Path Identifier VCI: Virtual Circuit Identifier
5

## Slide 10: TP, VPs, and VCs
TP: Transmission Path VP: Virtual Path
VC: Virtual Circuit
10 of 39

## Slide 11: Examples of VPs and VCs
10 of 39

## Slide 12: ATM Switching
Forwarding Table
VP switch (use only VPI)
* Most switches
VPC switch (use both VPIs and VCIs)
* Boundaries switches

## Slide 13: Connection oriented (Supports QoS)
ATM
Fast packet switching
  fixed length packets (cells)
Integration of different traffic types
  voice, data, video
Disadvantages
  Complex
  Expensive
  Not widely adopted

## Slide 14: MPLS Positioning
Combine the forwarding algorithm used
in ATM with IP
IP
ATM
MPLS
Packet Forwarding
Virtual Circuit Switching
Hybrid

## Slide 15: MPLS Overview
Switch data according to its Label (tag)
  look up in table
  determine next hop
  substitute new label
Do not pay attention to
  network and transport protocols
   Multiprotocol
Switching for IP and non-IP
Signaling protocol based on IP

## Slide 16: Outline
Motivation
MPLS Basics
Operation
Protocol Stack Architecture
Advantages and Disadvantages

## Slide 17: MPLS in the protocol stack
Between Layer 2 and Layer 3
MPLS
SDH: Synchronous Digital Hierarchy (optical fiber)

## Slide 18: MPLS Characteristics
RSVP: Resource Reservation Protocol
Flow Management
Independent of L2 and L3 protocols
Maps IP-addresses to fixed length labels
Interfaces to existing routing protocols (RSVP, OSPF)
Supports ATM, Frame-Relay and Ethernet

## Slide 19: Label
Generic label format
19
Shim: A thin, often tapered piece of material, such as wood, stone,
or metal, used to fill gaps, make something level, or adjust something to fit properly.
bits
…http://www.thefreedictionary.com/

## Slide 20: Label Distribution
Not specify a single method for label
distribution
Routing support for label exchange
  BGP and RSVP can piggyback the label information
IETF defines signal and management
  label distribution protocol (LDP)
Extension of LDP protocol
  support explicit routing based on QoS

## Slide 21: Label Insertion
Data Link Frame
IEEE 802 MAC Frame
ATM Cell
Frame Relay Frame

## Slide 22: MPLS Terminology
LDP: Label Distribution Protocol
LSP: Label Switched Path
FEC: Forwarding Equivalence Class
LSR: Label Switching Router
LER: Label Edge Router

## Slide 23: Label Edge Router (LER)
Edge of an MPLS network
Assigns and removes packet labels
Support multiple ports
  frame relay
  ATM
  Ethernet
  etc.

## Slide 24: Label Switching Router (LSR)
High speed router in the core on an
MPLS network
ATM switches can be used as LSR
  no hardware modification
  label switching is equivalent to VP and VC
switching

## Slide 25: LER and LSR Position
(Label Switched Path)

## Slide 26: Forward Equivalence Class (FEC)
Represent group of packets
  share same requirements for their transport
Packet Assignment
  assignment to each packet
  only one time at entry point

## Slide 27: Label-Switched Path (LSP)
A path is established before the data
transmission starts
A path is a representation of a Forward
Equivalence Class (FEC)

## Slide 28: LSP Setup
Hop-by-hop routing
  each LSR independently selects next hop for a given FEC
Explicit routing
  similar to source routing
(sender specify the route of the packet)
  ingress LSR specifies the list of nodes through
which the packet traverses
LSP setup for an FEC is unidirectional
  return traffic must use another LSP

## Slide 29: Label Distribution Protocol (LDP)
Application layer protocol
  for label binding distribution info to LSRs
  map FECs to labels (create LSP)
  LDP sessions are established between LDP peers in the MPLS network
(not necessarily adjacent).
  Sometimes employs OSPF or BGP

## Slide 30: LDP message types
Discovery messages
  announce/maintain the presence of an LSR
Session messages
  establish/maintain/terminate sessions between
LDP peers
Advertisement messages
  create, change, and delete label mappings for
FECs
Notification messages
  provide advisory info and signal error information

## Slide 31: Outline
Motivation
MPLS Basics
Operation
Protocol Stack Architecture
Advantages and Disadvantages

## Slide 32: Route at Edge, Switch in Core
IP Forwarding
LABEL SWITCHING
IP Forwarding
IP
IP #L1
IP #L2
IP #L3
IP

## Slide 33: MPLS: How does it work?
33
UDP-Hello
UDP-Hello
TCP-open
TIME
Label request
IP
Label mapping
#L2
Initialization(s)

## Slide 34: MPLS Operation
Five Steps
  label creation and distribution
  table creation at each router
  label-switched path creation
  label insertion/table lookup
  packet forwarding

## Slide 35: Step 1 :Label creation and distribution
First, routers bind a label to a specific FEC
Then build their tables
Using LDP
  downstream routers initiate the distribution of labels and the label/FEC binding
  negotiate traffic-related characteristics and MPLS
capabilities
A reliable and ordered transport protocol should be used for the signaling protocol

## Slide 36: Step 2: Table creation
On receipt of label bindings each LSR creates
entries in the label information base (LIB)
Table specifies the mapping between a label and an FEC
  mapping between the input port and input label table to the output port and output label table
  entries are updated whenever renegotiation of
label bindings occurs

## Slide 37
Example of
Label Information Base (LIB) Table
Input Port | Incoming Port Label | Output Port | Outgoing Port Label
1 | 3 | 3 | 6
2 | 9 | 1 | 7

## Slide 38: MPLS Label Distribution
Intf In | Label In |  |  | Dest | Intf Out
3 |  | 0.40 |  | 47.1 | 1
Intf In | Label In |  |  | Dest | Intf Out | Label Out |  | 
3 |  | 0.50 |  | 47.1 | 1 |  | 0.40 | 
47.1
47.2
47.3
1
2
3
1
2
1
2
3
3
Intf In | Dest | Intf Out | Label Out |  | 
3 | 47.1 | 1 |  | 0.50 | 
Mapping: 0.40
Request: 47.1

## Slide 39: Label Switched Path (LSP)
Intf In | Label In |  |  | Dest | Intf Out
3 |  | 0.40 |  | 47.1 | 1
Intf In | Label In |  |  | Dest | Intf Out | Label Out |  | 
3 |  | 0.50 |  | 47.1 | 1 |  | 0.40 | 
47.2
1
2
3
1 47
2
1
2
47.3 3
Intf In | Dest | Intf Out | Label Out |  | 
3 | 47.1 | 1 |  | 0.50 | 
IP 47.1.1.1
IP 47.1.1.1 .1
3

## Slide 40: Step 3: Label switched path creation
LSPs are created in the reverse direction to the creation of entries in the LIBs.

## Slide 41: MPLS Example
LER 1
LER 2
LER 3
LER 4
Source
Destination
LSR 3
LSR 1
LSR 2

## Slide 42: Step 4: Label insertion/table-lookup
First router (LER1) uses LIB table to find the next hop and request a label for the specific FEC
Subsequent routers just use the label to find the next hop
Once the packet reaches the egress LSR (LER3), the label is removed and the packet is supplied to the destination

## Slide 43: Step 5: Packet forwarding
For first time packet
  LER1 may not have any labels
  (In IP) find the longest add match for next hop
  Let LSR1 be the next hop for LER1.
LER1 will initiate a label request toward LSR1
This request will propagate through the
network (green lines)

## Slide 44: MPLS Operation Example
LER 1
LER 2
LER 3
LER 4
Source
Destination
LSR 3
LSR 1
LSR 2
Label Request

## Slide 45: Step 5 (cont.)
Label downstream (LER3 LSR …  LER1)
The LSP setup (blue lines) uses LDP or any other signaling protocol.
LER1 will insert the label and forward the packet to LSR1

## Slide 46: MPLS Operation Example
LER 1
LER 2
LER 3
LER 4
Source
Destination
LSR 3
LSR 1
LSR 2
Label Request Label Distribution

## Slide 47: Step 5 (cont.)
Each subsequent LSR (LSR2,LSR3)
  examine label in received packet
  replace it with outgoing label
  forward it
When reaches LER4, label is removed
  leave MPLS domain and deliver to the destination
Actual data path followed by the packet is the red line

## Slide 48: MPLS Operation Example
LER 1
LER 2
LER 3
LER 4
Source
Destination
LSR 3
LSR 1
LSR 2
Label Request Label Distribution Data Flow

## Slide 49: Tunneling in MPLS
Control the entire path of a packet without explicitly specifying the intermediate routers.
  Creating tunnels through the intermediary routers that can span multiple segments.
MPLS based VPNs.

## Slide 50: MPLS network application (MPLS L2 VPN)
http://www.centecnetworks.com/en/SolutionList.asp?ID=77
customer edge (CE) routers provider edge (PE) routers

## Slide 51: Tunneling in MPLS

## Slide 52: Outline
Motivation
MPLS Basics
Operation
Protocol Stack Architecture
Advantages and Disadvantages

## Slide 53: MPLS Protocol Stack Architecture

## Slide 54: Outline
Motivation
Basics
Operation
Protocol Stack Architecture
Advantages and Disadvantages

## Slide 55: MPLS Advantages
Improves packet-forwarding
performance in the network
Supports QoS and CoS for service
differentiation
Supports network scalability
Integrates IP and ATM in the network
Builds interoperable networks

## Slide 56: MPLS Disadvantages
An additional layer is added
The router has to understand MPLS

## Slide 57: Transport Network in Legacy 2G/2.5G
http://lteuniversity.com/get_trained/expert_opinion1/b/skrishnamurthy/archive/2013/04/01/why-ethernet-backhaul.aspx

## Slide 58: Unified Backhaul and Core Network in
2G/2.5G/3G/4G Networks
customer edge (CE) routers
http://lteuniversity.com/get_trained/expert_opinion1/b/skrishnamurthy/archive/2013/04/01/why-ethernet-backhaul.aspx
customer edge (CE) routers provider edge (PE) routers

## Slide 59: References
“MPLS Introduction”, Yun Teng, Dept. of Computer
Science, UMBC
“MPLS Tutorial and Operational Experiences”, Peter Ashwood-Smith, Bilel Jamoussi, October, 1999